| X National Forest Y Ranger District Fire Effects Monitoring Report |  |
| --- | --- |

Unit:	Castilleja Units 97, 98, 99	            Date: May 30-31, 2010

Fuel Type: Dry pine, grass, few shrubs

Fuel Model: 9

Acres Planned: 100

Acres Burned: 100

FEMO: Smokey Bear

FEMO (t): Wyle Coyote

Purpose and Resource Management Goals:

The primary purpose of this prescribed burn is to …

Specific Prescribed Fire Objectives:

- Burn 50%-100% of each unit

- Reduce 1 hr. fuels by 50%-100%

- Reduce 10 and 100hr. fuels by 30%-60%

- Reduce 1000hr. fuels by 10%-50%

Caption for photo

Site Description:

The burn unit is on a 20% slope with south aspect. This is a third entry in an even-age stand of ponderosa pines between 16-20” dbh. The understory is mostly Idaho fescue with scattered patches of bitterbrush and ceanothus.

May 30, 2010 (Units 97-98)

1035	Briefing - decision was made to begin lighting in Unit 97 with the North Burn Group.

1210	Test fire lit at NE corner of Unit 97.  Ten-foot spacing between lighters with a 50’ lag produced 6-12” flame lengths with strips closing in approximately five minutes. Good consumption of thick needle cast occurred about 15 minutes after lighting.

1220	Commenced ignition in NE corner with 10’ spacing between lighters. The strips did not close	uniformly, failed to come together in some shaded places and/or where the needlecast is less than 1”	deep.  In areas where needle cast is thicker and fuels are exposed to sun, the strips closed and 	objectives were met.

1248	Smoke column drifted to the top of Blue Ridge and dispersed to SW at 4000’elevation.

1310	Approximately 70% of the 1-hour fuels and 35% of the 10 and 100-hour fuels were consumed, meeting 	burn objectives in these categories.  About 10% consumption of 1000-hour fuels was observed.	Bitterbrush burned sporadically in areas of thick needlecast and infrequently in areas where the needlecast	was lighter. Bitterbrush consumption was marginal; except in rare instances, Ceanothus was not burning.

1400	Lighting completed on Unit 97. Paused to collect remaining slash fuel and evaluate whether it would be sufficient for the rest of the day.  (Note: 80 gallons was just enough for the day).

1435	South Burn Group commenced ignition on Unit 98.  Fire was very active with frequent firewhirls.

1445	Spot fire 5’ off of  E line caused by ember fall; contained at 3 square feet.

1450	Smoke was pulling in toward center of the unit. Objectives were being met, albeit on the low end.

1500	More of the 10, 100 and 1000-hour fuels were catching, but still very little of the shrub component. Ignition pattern was switched to dot lighting.

1520	Some bitterbrush torching was observed, estimated at 20%.

1530	Burn strips came together well in most places. The best fire effects of the day occurred from this point	through the rest of the burn, although the bitterbrush continued to burn sporadically at best.

1615	Burning completed on Unit 23.  Overall, the burned units met the prescription on the low end. The	majority of each unit got burned, and a mosaic pattern was provided by areas of light needlecast and	dense bitterbrush.

1630	Surface fire died out quickly after ignition stopped.  The only remaining heat was in the few heavies that	had caught and in a few smoldering places on the south line.

1730	During the AAR the Burn Boss decided to continue with Unit 99 on the following day and adapt for success by starting later in the day.

May 31, 2010 (Unit 99)

1230	Briefing.

1355	Test fire lit in SE corner of Unit 12. Strip lighting commenced, but fire behavior was not very active and	lighting was paused.

1435	Inversion cleared. Flame lengths were 6-18”. ROS estimated at 1 chain/hour. Fire behavior was similar to	that seen at the same time on the previous day. Strips burned together well in areas of thick needlecast and	sunlight, but patches of thin needlecast and/or bitterbrush did not	burn and the fire did not carry uniformly	in shaded areas.

1455	Less than 5% of the bitterbrush was torching, and none of the Ceanothus. ROS about 5 chains/hour.

1515	Hand-lighting individual bitterbrush was used with good effect in some areas.

1545	Ignition completed. Fire behavior subsided sharply as the shadows lengthened.

Fire Effects and Meeting Objectives:

Fire behavior remained moderate to low depending on firing techniques through the burn period. Strip-head firing and dot pattern produced good results with 30% consumption in the standing brush. The objectives for 1-hr, 10-hr, and 100-hr fuels were met in the low end of the desired ranges. Roughly 10% of downed logs were charred, but none were consumed. Some isolated single tree torching and group torching was observed in areas with denser shrub understory and vertical continuity.

Caption for photo

Weather Observations: 05/30/2010

| Time | Location | Wind Direction |  | Wind Speed (mph) | Dry Bulb (°F) | Wet Bulb (°F) | RH (%) | Cloud Cover (%) | POI (%) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1000 | DP2 | variable |  | light | 41 | 39 | 65 | Cirrus in west, 10 | 10 |
| 1100 | Test fire | N |  | light | 51 | 45 | 60 | Altostratus in west, 20 | 20 |
| 1200 | interior | NE |  | light | 60 | 49 | 50 | Scattered cirrus , 25 | 30 |
| 1300 | NE corner | N-NW |  | 1-3 | 65 | 52 | 44 | Clear | 30 |
| 1400 | NE corner | NW |  | 2-5 | 67 | 53 | 39 | Clear | 30 |
| 1500 | SE corner | N |  | 2-5 | 68 | 53 | 39 | Clear | 30 |
| 1530 | SE corner | NE |  | 2-5 | 70 | 53 | 35 | Clear | 30 |
| 1600 | SE corner | N |  | 5-7 | 68 | 54 | 42 | Cirrus in west, 10 | 20 |
| 1645 | DP2 | N |  | 2-5 | 65 | 52 | 45 | Clear | 20 |

Weather Observations: 05/31/2010

| Time | Location | Wind Direction |  | Wind Speed (mph) | Dry Bulb (°F) | Wet Bulb (°F) | RH (%) | Cloud Cover (%) | POI (%) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1200 | DP2 | NE |  | light | 60 | 49 | 50 | Scattered cirrus , 25 | 30 |
| 1300 | Test fire | N-NW |  | 1-3 | 65 | 52 | 44 | Clear | 30 |
| 1400 | DP1 | NW |  | 2-5 | 67 | 53 | 39 | Clear | 30 |
| 1500 | DP1 | N |  | 2-5 | 68 | 53 | 39 | Clear | 30 |
| 1530 | S flank | NE |  | 2-5 | 70 | 53 | 35 | Clear | 30 |
| 1600 | DP2 | N |  | 5-7 | 68 | 54 | 42 | Cirrus in west, 10 | 20 |

Caption for photo					Caption for photo